## Slide 1: The Controller Placement Problem in SDN: A Survey
Guodong Wang, Yanxiao Zhao, Jun Huang, and Wei Wang

## Slide 2: SDN Benefits
Simplifying the network management
Improving the efficiency of network utilization
Enabling network innovations

## Slide 3: Controller Placement Problem
Openflow standard (One controller)
Scalability and performance issues when the network scale continually expands.
Multiple Controller Approaches
Controller Placement Problem
  Undirected Graph G = (V,E)
  Dijkstra used to represent distance between switches
  Solution Set: {k; C; S} (k – centre problem)

## Slide 4: Layered Structure

## Slide 5: Objectives of Controller Placement
Minimize latency between controllers and their associated switches => Packet propagation latency
  K center problem
  NP hard to K-median problem
Enhance reliability and resilience of the network
  Use of redundant links (Survivor)
  Path diversity => increases survivability
Minimize deployment cost and energy consumption
  90 % energy lost during idle time

## Slide 6: Algorithms
Already well known clustering algorithms
  K centre algo like greedy, local search
  K means
They use euclidean distance which is not appropriate
They require a Metric Space
  No 3 is problematic

## Slide 7: Proposed Algorithm - CNPA
Cluster based Network Partition Algorithm
Preprocessing
  Adjacency matrix
  Co-ordinates (Google Map)
  Distance (Haversine Formula)
  Switch to switch distance using Dijkstra
Apply CNPA algorithm which keeps dividing the network into clusters until k centers are formed

## Slide 8: CNPA
Randomly Select center
Find each nodes' sum distance from all other nodes and select node with minimum as centroid
Second center -> furthest from clusters centroid
Centroid (c1) and center (c2) as initial centers and assign nodes using distance measures ( d(ni, c1) and d(ni, c2) ) and compare
Keep repeating this process from step 2 until k sub networks are formed

## Slide 9: Network Details
34 nodes (all over Canada to USA)
43 links in total
Maximum distance (shortest path distance) is 3120 miles (50 ms round trip)
Experiment done 100 times
Propagation Latency = distance(m)/(2x10^8 m/s)

## Slide 10: CNPA for k = 5

## Slide 12: CNPA for k = 6